## Slide 1: Combating Biofouling
Garrett Brogan, Nick Dalton, and Sean Fallon

## Slide 2: What is the Issue?
Biofouling is incredibly aggressive in
San Juan Bay
Sector San Juan cutters are budgeted for only one in-water cleaning a year
Biofouling over time will reduce a ship’s top speed and decrease its fuel efficiency

## Slide 3: Video Overview

## Slide 4: Our Approach
Early on, it was discovered that data needed to make quantitative and accurate conclusions was not available
Three Main Deliverables:
Data collection
and analysis protocol
Recommendations for alternative antifouling coatings
Recommendations
for alternative
hull cleaning tools and techniques
I
II
III
Source: https://upload.wikimedia.org/wikipedia/commons/d/d6/Dry_docking.8.JPG
Source: https://commons.wikimedia.org/wiki/File:Cleaning_the_hull_3.jpg
Notes: Templar52 (Photographer). (2008, June 30). Dry docking [digital image]. Retrieved from https://upload.wikimedia.org/wikipedia/commons/d/d6/Dry_docking.8.JPG
Shebs, Stan (Photographer). (2005, November 3). Cleaning the Hull [digital image]. Retrieved from https://commons.wikimedia.org/wiki/File:Cleaning_the_hull_3.jpg

## Slide 5: 1st Deliverable: Data Protocol
Designed a protocol to collect and analyze the necessary data to illustrate the potential savings in fuel costs for an altered cleaning schedule
Data necessary:
    Biofouling Accumulation
    Speed and associated RPM
    Fuel Burn
    Distances Traveled
    Gallons per hour
Source: www.dvidshub.net
Notes: Barney, Mark. Cutter Heriberto Hernandez [Online Image]. (2015). Retrieved December 7, 2015 from www.dvidshub.net

## Slide 6: Data: Biofouling Accumulation
Why:
  To illustrate the nature of biofouling accumulation in sector San Juan
  To base initial estimates for new cleaning schedule off of
How:
  Use an underwater video camera with extension pole to record the hull fouling
    This will occur every time a ship returns to base and before it goes underway
  Analyze the video using a visual fouling guide and input fouling data into the fouling form

## Slide 7
Cutter
Hull
6 ft
~ 4 ft
2 ft
4 ft
10 ft
Underwater Camera Setup Dimensions

## Slide 8: Analysis: Biofouling Accumulation

## Slide 9: Example Biofouling Accumulation
Data collected via analysis of underwater hull footage
(Data in the chart is self generated)

## Slide 10: Example Biofouling Accumulation
How biofouling accelerates
(Self-Generated Data)

## Slide 11: Data: Fuel Burn and Distances Traveled
Why:
  Necessary to calculate cost savings from altered cleaning schedule
How:
  Fuel burn data from round sheets
  Distances from Log-Weather Observation and Operational Summary Sheet

## Slide 12: Analysis: Fuel Burn and Distances Traveled

## Slide 13: Example Fuel Efficiency Loss
Date (Week) | Self Generated Fuel Burn Data |  |  | 
 | Fuel Burn (gal) | Distance Travelled (NM) | NM/Gallons | Gallons/Nautical Mile
1/7 | 148.6 | 81.48 | 0.548317631 | 1.823760432
2/7 | 148.6 | 81.2331 | 0.546656124 | 1.829303572
3/7 | 148.6 | 80.9862 | 0.544994616 | 1.834880511
4/7 | 148.6 | 80.7393 | 0.543333109 | 1.840491557
5/7 | 148.6 | 80.4924 | 0.541671602 | 1.846137027
6/7 | 148.6 | 80.2455 | 0.540010094 | 1.851817236
1 | 148.6 | 79.9986 | 0.538348587 | 1.857532507
1 1/7 | 148.6 | 79.7517 | 0.536687079 | 1.863283165
1 2/7 | 148.6 | 79.5048 | 0.535025572 | 1.86906954
1 3/7 | 148.6 | 79.2579 | 0.533364065 | 1.874891967
1 4/7 | 148.6 | 79.011 | 0.531702557 | 1.880750782
1 5/7 | 148.6 | 78.7641 | 0.53004105 | 1.886646327
1 6/7 | 148.6 | 78.5172 | 0.528379542 | 1.892578951
2 | 148.6 | 78.2703 | 0.526718035 | 1.898549003
2 1/7 | 148.6 | 78.0234 | 0.525056528 | 1.904556838
2 2/7 | 148.6 | 77.7765 | 0.52339502 | 1.910602817
2 3/7 | 148.6 | 77.5296 | 0.521733513 | 1.916687304
2 4/7 | 148.6 | 77.2827 | 0.520072005 | 1.922810668
2 5/7 | 148.6 | 77.0358 | 0.518410498 | 1.928973283
2 6/7 | 148.6 | 76.7889 | 0.516748991 | 1.935175527
3 | 148.6 | 76.542 | 0.515087483 | 1.941417784
Data continues on to 18 weeks

## Slide 14: Example Fuel Efficiency Loss
Chart: Mid Speed Fuel Burn/Distance over Time
| 9 | 9
Cleaning Intervals | 0 | 3
 | 1
 | 1
 | 1
 | 1
 | 1
 | 1
 | 1
 | 1
 | 1
Chart: Mid Speed Fuel Burn/Distance over Time
 | 1
 | 1
 | 1
 | 1
 | 1
 | 1
 | 1
 | 1
 | 1
Cleaning Intervals | 0 | 3
Cleaning Interval 2 | 0 | 3
Doubling Cleaning Frequency
Tripling Cleaning Frequency

## Slide 15: 2nd Deliverable: Antifouling Recommendations
Two Types of Antifouling coatings:
  Non-Biocidal
    Creates a low friction surface so fouling may be removed easily
  Biocidal
    Releases chemicals to prevent biofouling
Most common biocidal paint is an ablative
  Ablative paints work by “wearing away” while in the water and are typically much softer than most other coatings

## Slide 16: Current Vessel Coating
Cutters employ International Interspeed BRA 640
  Copper ablative
COs and contract divers state the paint is soft
Paint is worn away after cleanings
  Reduces effectiveness
Prevents coating from fully succeeding
Screenshot from a Sector San Juan Cleaning
Provided by USCG Sector San Juan
Notes: Screenshot from USCGC Reef Shark Hull Cleaning. [Video Image]. (2015).

## Slide 17: Time For a Change
Navy is halting use of copper based products
Will also work better with more frequent cleanings
Harder paint of a different type
Due to this, we believe a Fouling Release may be more suitable

## Slide 18: SWOT Analysis

## Slide 19: Antifouling “Playbook”
Following this suggestion, we have found the following coatings to be good candidates:
Once an effective cleaning interval has been determined, we believe these coatings may offer a better defense against biofouling
  SigmaGlide 1290
  International 700
  International 900

## Slide 20: 3rd Deliverable: Cleaning Techniques
Employed a three part methodology in our study of different hull cleaning techniques
1) Learned the current techniques used by Coast Guard contractors
2) Consulted scientific literature
3) Drew conclusions that will make cleanings more efficient

## Slide 21: Summary: Implement Groomings to Cleanings
Groomings are light cleanings, using soft bristled brushes and materials with lower coefficients of frictions
  Nylon-bristled brushes
  Circular brushing methods
Once the macrofouling is removed,
applying groomings to the hull will
remove microfouling
  This reduces the environment
  for the macrofouling to grow,
  optimizing cleanings and lengthening
  the time between cleanings
Source: www.biokleen.com
Notes:   [Biokleen Boat Brush]. Retrieved December 7, 2015 from www.biokleen.com

## Slide 22: Future Possibilities
Scientific literature has suggested the possibility of autonomous hull cleaning tools
Still in the trial stages, but could revolutionize the way in which hulls are cleaned
  Howell Ultrasonic Transducer

## Slide 23: Summary
Save Sector San Juan money lost due to fuel inefficiencies
Develop a protocol to produce cleaning schedules
Propose alternative Antifouling Technologies
Propose new hull cleaning tools and techniques
Determine data that needs to be collected
Analyze current data collected
Research
Antifouling
on the market
Compare Antifouling with SWOT Analysis
Analyze current
hull cleaning procedure
Research hull cleaning techniques

## Slide 24: Thank you for your time!

## Slide 25: References
Barney, Mark. Cutter Heriberto Hernandez [Online Image]. (2015). Retrieved December 7, 2015 from www.dvidshub.net
  [Biokleen Boat Brush]. Retrieved December 7, 2015 from www.biokleen.com
Screenshot from USCGC Reef Shark Hull Cleaning. [Video Image]. (2015).
Shebs, Stan (Photographer). (2005, November 3). Cleaning the Hull [digital image]. Retrieved from https://commons.wikimedia.org/wiki/File:Cleaning_the_hull_3.jpg
Templar52 (Photographer). (2008, June 30). Dry docking [digital image]. Retrieved from https://upload.wikimedia.org/wikipedia/commons/d/d6/Dry_docking.8.JPG