## Slide 1: LIVE FIRE TRAINING STRUCTURE
El Cuerpo de Bomberos de Costa Rica
Hannah Borges, Ava Schlesinger, Liam Spence, Connor Sullivan
[1]

## Slide 2: TEAM MEMBERS Connor Sullivan Hannah Borges Ava Schlesinger Liam Spence
Mechanical Engineering
Mechanical Engineering
Biomedical Engineering
Civil Engineering

## Slide 3: PROJECT GOAL
The goal of our project was to investigate and define the elements needed to design a live fire training structure on the Bomberos’ training ground. We focused on maintaining high levels of safety with respect to feasibility to ensure that the training structure was well-received by the Bomberos.
[2]

## Slide 4: SAN JOSÉ, COSTA RICA
Dry season occurs between November and April;
Greater Metropolitan Area (GAM) accounts for 4% of Costa Rica’s land;
More than 50% of country’s population lives in the GAM;
[3]

## Slide 5: WHO ARE THE BOMBEROS?
Organization responsible for controlling fires and maintaining the safety of Costa Rican citizens;
Trained at the National Fire Academy;
Requested a design for a new fire training tower.
[4]

## Slide 6: FIRE TRAINING STRUCTURES
A decrease in fire incidents led to the necessity of fire simulators.
To be prepared for real situations, firefighters need hands-on skills development.
There are many different simulators that integrate modern construction models and techniques.
[5]

## Slide 7: TIMELINE
Research of Fire Protection code
OBJECTIVE 2
Establish set of requirements
OBJECTIVE 4
Interviews with fire professionals
OBJECTIVE 3
Background research of training structures
OBJECTIVE 1
Modeling and design of tower
OBJECTIVE 5

## Slide 8: TIMELINE
Research of Fire Protection code
OBJECTIVE 2
Establish set of requirements
OBJECTIVE 4
Interviews with fire professionals
OBJECTIVE 3
Background research of training structures
OBJECTIVE 1
Modeling and design of tower
OBJECTIVE 5

## Slide 9: Current Tower
Open-air
Rappelling exercises
Training with hoses on stairwells
Not compatible for conducting live fire evolutions
[6]
Notes: .

## Slide 10: NFPA 1001 Obscure vision Carry unconscious victims Rope Rescue and Laddering Ascend and descend fixed-rope systems Place, mount and dismount ladders Any evolution conducted in a burn room Search and Rescue Live-Fire

## Slide 11: ORIGINAL REQUESTS ENCLOSED STAIRWELL LIQUID PETROLEUM GAS BELOW-GRADE BASEMENT WATER COLLECTION 01 04 03 02
Practice basement fire evolutions.
Separate from the main body of the structure.
Fuel system for interior fires.
Reuse water in future training exercises.

## Slide 12: NFPA COMPLIANT OPTIONS
enclosed
OPTION 1
OPTION 2
OPTION 3
BASEMENT
FUEL SYSTEM
STAIRWELL
WATER COLLECTION
Full basement
No live-fire
Half below-grade
Live-fire
Separate stairwell,
windows and live-fire
Separate stairwell
enclosed, no fire
LPG
Propane
Wooden pallets & hay
Interior collection system
Exterior drain system

## Slide 13: DIFFERENT TOWER DESIGNS TOWER A TOWER B TOWER C
Concrete Structure
Wooden Pallets and Hay
No Basement
Footprint > 150 m2
Concrete Structure
LPG Gas
Half-Basement
Footprint of 64 m2
Steel Structure
No Fires in Basement
Full Basement
Footprint of 36 m2
[7]
[8]
[9]

## Slide 14: PUGH MATRIX
Criteria | Weight | Tower A |  | Tower B |  | Tower C | 
 |  | Score | Total | Score | Total | Score | Total
Cost | 3 | 5 | 15 | 2 | 6 | 2 | 6
Performance | 4 | 4 | 16 | 4 | 16 | 3 | 12
Safety | 5 | 5 | 25 | 2 | 10 | 5 | 25
Visual Appeal | 2 | 3 | 6 | 3 | 6 | 4 | 8
Eco-Friendliness | 3 | 2 | 6 | 5 | 15 | 1 | 3
Effectiveness | 4 | 3 | 12 | 3 | 12 | 5 | 20
 | Sum |  | 80 |  | 65 |  | 74

## Slide 15: OUR FINAL RECOMMENDATIONS Stairwell Basement LPG Concrete Thermal Imaging Ventilation
Cleaner fuel with easier control.
Enclosed staircase with no real fire.
Half-basement is safer and complies with NFPA code.
More resistant to fire over time in comparison to steel.
Handheld equipment carried by firefighters.
Ventilation system with fans to monitor smoke levels.

## Slide 16: Floor Plans Iterations
Notes: Ava

## Slide 17: Revit Model

## Slide 18: COST SUMMARY
Material | Cost (USD)
Cement | 51361.43
Rebar | 24299.46
Tie Wire | 520.93
Pipes | 12894.34
Padgenite | 65600
2 Cameras | 6490
Total (USD) | 161166.16
Total (CRC) | 98582116.75

## Slide 19: FUTURE WORK AIR FILTRATION WATER FILTRATION
In addition to water collection system, integrate previous IQP filtration system.
Due to the high cost of HEPA filters, we recommend future research on a more cost-effective filtration.

## Slide 20: Questions?
Thank you to our sponsors and advisors for helping us with this project!
[10]

## Slide 21: REFERENCES
REFERENCES
Boie, T., Muenchow, K., Vangos, T., & Vodola, K. (2018). Designing a Sustainable Water Supply Network for El Cuerpo de Bomberos Training Practices. Worcester; Worcester Polytechnic Institute.
Ciolfi, J., Nippert, K., Picho, K., Spalding, L. (2020). Exploration of A Robot Development Program for the Costa Rican Fire Department. Worcester; Worcester Polytechnic Institute.
Mason, Mike. (2006, July 10). Live Fire Training - Part 2. Firehouse. https://www.firehouse.com/operations-training/article/10505079/live-fire-training-part-2
National Fire Protection Association. (2021). NFPA: Overview. https://www.nfpa.org/overview
O’Donnell, R. (2015) Global Trends in Fire Training Facilities. Firehouse. https://www.firehouse.com/home/article/12092033/firefighter-training-trends-in-fire-training-facilities-around-the-world
Spell, J. (2020, October 19). A firefighter’s guide to fireground search and rescue- part 2. FireRescue1. https://www.firerescue1.com/fire-products/rescue-equipment/articles/a-firefighters-guide-to-fireground-search-and-rescue-part-2-TRLszcH6HvQpBhlJ/
www.mrrabbit.cr. (2020). Bomberos Costa Rica. http://www.bomberos.go.cr/.
IMAGE REFERENCES
https://www.draeger.com/Library/Media/containerized-live-fire-training-system-prepare-to-train-3-2-d-9083-2016.jpg?imwidth=480
https://media.defense.gov/2019/Aug/28/2002176592/-1/-1/0/190821-O-VI420-0216C.JPG
https://www.google.com/maps/place/National+Fire+Academy/@10.2457299,-84.2867847,7.79z/data=!4m5!3m4!1s0x8fa0e3b309439e9d:0x22e5358dbedfb05d!8m2!3d9.8963261!4d-84.0448266
http://www.usexpatcostarica.com/wp-content/uploads/2017/04/Fire-Department-315x420.jpeg
http://www.asoquemcr.com/project03.html
https://www.pinterest.com/pin/320459329706116951/
MA Firefighting Academy. (n.d.) Burn Building.
WHP Trainingtowers. (2015) Custom 1st Alarm - Four Story Rope Tower.
https://www.pinterest.de/pin/299489443970081516/
https://upload.wikimedia.org/wikipedia/commons/8/8f/Fire_inside_an_abandoned_convent_in_Massueville%2C_Quebec%2C_Canada.jpg