## Slide 1: Distributed Virtual Environment for the Real-time Test and Evaluation of Radar Systems
Matthew Lyon James Montgomery Lucas Scotta
13 October 2010
Advisors: George T. Heineman Hugh Lauer Edward A. Clancy
MIT Lincoln Laboratory Supervisor: D. Seth Hunter
This work was sponsored by the Department of the Air Force under Contract No. FA8721-05-C-0002. Opinions, interpretations, recommendations and conclusions are those of the authors and are not necessarily endorsed by the United States Government.
Notes: 1
1

## Slide 2: High-level Radar Overview
How does radar work?
  Transmitter emits a short electromagnetic pulse
  Pulse hits target, reflects back
  Receiver listens for return energy
Radar processing software
  Control radar hardware
  Convert return energy to useful information
Radar Uses
  Weather sensing
  Remote Imaging
  Track moving objects (our focus)
Radar
Processing
Software
Radar Control Msg.
Pulse Aux Data
Radar
Sub systems
Pulse
Return

## Slide 3: Radar Simulation
Use software to simulate the radar hardware, targets, and environment
Need for testing before deployment
Saves time & money, don’t need physical hardware and real-life targets to test software
KMAR Simulator Developed at MIT LL, currently used for radar simulation
Radar
Processing
Software
Pulse Aux Data
Simulator
Simulated
Hardware
Simulated targets and environment
Radar Control Msg.

## Slide 4: Current + Desired Simulator Features
KMAR Simulator
Features
  Real-time, closed-loop
  Complex environmental effects
  High-fidelity waveforms
  Trajectory models
  Radar cross section models
Limitations
  Single-machine
  Typically supports only up to 64 targets
  Difficult to extend

## Slide 5: Current + Desired Simulator Features
Requirements
  Scalable to thousands of targets
  Extensible to different types of targets and radar hardware
  Design must support major features of KMAR simulator
Goals
  Design an extensible simulator architecture
  Implement a working prototype to demonstrate scalability
  Use modern software techniques / tools
KMAR Simulator
Features
  Real-time, closed-loop
  Complex environmental effects
  High-fidelity waveforms
  Trajectory models
  Radar cross section models
Limitations
  Single-machine
  Typically supports only up to 64 targets
  Difficult to extend
New Simulator

## Slide 6: Methodology and Resources
OASIS Simulator Framework
LL Staff
RTCL
Domain Literature
ROSA II

## Slide 7: Design Overview
Hardware Simulator
Environment Simulator
Pulse
Return
Radar Control Program
Control message
Processed
Return

## Slide 8: Event-based simulation
Models
  Maintain state
  Process events to update state
  Schedule events on other models
Simulation engine
Event Queue
Models
Simulation Time
Model State
Schedule Event
Process Event
Simulation Engine
  Maintains simulation time
  Contains event queue
Events
  Associate an action with a time

## Slide 9: Radar in Detail

## Slide 10: Models and Events
Transmitter Model
Receiver Model
Target Model
Pulse Event
Return Event

## Slide 11: Extensibility
Radar Cross Section
Trajectory
Target Class

## Slide 12: Layered Architecture
RTCL
Models
Simulation Engine
External components
User interface, External software
Domain-specific models and events
Maintains event queue, time
Based on OASIS simulation architecture
Adjacent layers interact during a simulation
Simulation control, logging
Middleware abstraction layer
Controller
Component
Inter-process communication
Communications middleware
Process base class

## Slide 13: Distributed Event-based simulation
Multiple simulation engines work together
  Run independently
  Separate event queues and models
  Exchange relevant events
  Synchronize simulation time
Hardware Simulator
Target Simulator
Engine
Models
Engine
Events
Models

## Slide 14: Scalability & Distributed Architecture
Hardware Simulator
Target Simulator B
Simulate targets 101-200
Target 2 thread
Target 1 thread
Target N thread
Pulse Event
…
Target Simulator A
Simulate targets 1-100
Target Simulator C
Simulate targets 201-300
Radar Control Program

## Slide 15: Simulator Implementation
Working prototype
  Multi-process, distributed
Complete test scenario
  Basic transmitter, receiver models
  Point source target model
Generic simulation engine
150 km
1
2
1 + 2

## Slide 16: Project Deliverables
  Design
    Passed Lincoln Laboratory Design Review
  Implementation
    Functional basic implementation code
  Documentation
    User and Developer Guide
    Doxygen source code comments
    MQP Report
  Testing
    Complete testing suite, with 80% code coverage
Design Review
Attendees
Marcia Powell
Jeffrey McHarg
Andrew Clough
Matt Leahy
Seth Hunter
Rich Taylor
Sam Reynolds
Greg Gimler

## Slide 17: Future Work
More realistic transmitter and receiver models
Implement advanced target radar cross sections
Load balancing
Realistic environment models
Direct Integration with ROSA

## Slide 18: Acknowledgements
Thanks to
  MIT Lincoln Laboratory
  Gary Ahlgren, John Nelson, Frank Robey
  Seth Hunter
  Marcia Powell, Andrew Clough, Greg Gimler, David Carpman, Matt Leahy
  George Heineman, Hugh Lauer, Ted Clancy
  Emily Anesta, Scot DeDeo, Adam Lewis
Questions?
Transmitter Model
Receiver Model
Target Model